## Slide 1: Assembly Language for x86 Processors 7th Edition
Chapter 7: Integer Arithmetic
(c) Pearson Education, 2015. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Slides prepared by the author
Revision date: 1/15/2014
Kip R. Irvine

## Slide 2: Chapter Overview
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and Unpacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 3: Shift and Rotate Instructions
Logical vs Arithmetic Shifts
SHL Instruction
SHR Instruction
SAL and SAR Instructions
ROL Instruction
ROR Instruction
RCL and RCR Instructions
SHLD/SHRD Instructions

## Slide 4: Logical Shift
A logical shift fills the newly created bit position with zero:

## Slide 5: Arithmetic Shift
An arithmetic shift fills the newly created bit position with a copy of the number’s sign bit:

## Slide 6: SHL Instruction
The SHL (shift left) instruction performs a logical left shift on the destination operand, filling the lowest bit with 0.
Operand types for SHL:
SHL reg,imm8
SHL mem,imm8
SHL reg,CL
SHL mem,CL
(Same for all shift and rotate instructions)

## Slide 7: Fast Multiplication
mov dl,5
shl dl,1
Shifting left 1 bit multiplies a number by 2
mov dl,5
shl dl,2 ; DL = 20
Shifting left n bits multiplies the operand by 2n
For example, 5 * 22 = 20

## Slide 8: SHR Instruction
The SHR (shift right) instruction performs a logical right shift on the destination operand. The highest bit position is filled with a zero.
mov dl,80
shr dl,1 ; DL = 40
shr dl,2 ; DL = 10
Shifting right n bits divides the operand by 2n

## Slide 9: SAL and SAR Instructions
SAL (shift arithmetic left) is identical to SHL.
SAR (shift arithmetic right) performs a right arithmetic shift on the destination operand.
An arithmetic shift preserves the number's sign.
mov dl,-80
sar dl,1 ; DL = -40
sar dl,2 ; DL = -10

## Slide 10: ROL Instruction
ROL (rotate) shifts each bit to the left
The highest bit is copied into both the Carry flag and into the lowest bit
No bits are lost
mov al,11110000b
rol al,1 ; AL = 11100001b
mov dl,3Fh
rol dl,4 ; DL = F3h

## Slide 11: ROR Instruction
ROR (rotate right) shifts each bit to the right
The lowest bit is copied into both the Carry flag and into the highest bit
No bits are lost
mov al,11110000b
ror al,1 ; AL = 01111000b
mov dl,3Fh
ror dl,4 ; DL = F3h

## Slide 12: RCL Instruction
RCL (rotate carry left) shifts each bit to the left
Copies the Carry flag to the least significant bit
Copies the most significant bit to the Carry flag
clc ; CF = 0
mov bl,88h ; CF,BL = 0 10001000b
rcl bl,1 ; CF,BL = 1 00010000b
rcl bl,1 ; CF,BL = 0 00100001b

## Slide 13: RCR Instruction
RCR (rotate carry right) shifts each bit to the right
Copies the Carry flag to the most significant bit
Copies the least significant bit to the Carry flag
stc ; CF = 1
mov ah,10h ; CF,AH = 1 00010000b
rcr ah,1 ; CF,AH = 0 10001000b

## Slide 14: SHLD Instruction
Shifts a destination operand a given number of bits to the left
The bit positions opened up by the shift are filled by the most significant bits of the source operand
The source operand is not affected
Syntax:
  SHLD destination, source, count
Operand types:
SHLD reg16/32, reg16/32, imm8/CL
SHLD mem16/32, reg16/32, imm8/CL

## Slide 15: SHLD Example
Shift count of 1:
mov al,11100000b
mov bl,10011101b
shld al,bl,1

## Slide 16: SHRD Instruction
Shifts a destination operand a given number of bits to the right
The bit positions opened up by the shift are filled by the least significant bits of the source operand
The source operand is not affected
Syntax:
  SHRD destination, source, count
Operand types:
SHRD reg16/32, reg16/32, imm8/CL
SHRD mem16/32, reg16/32, imm8/CL

## Slide 17: SHRD Example
Shift count of 1:
mov al,11000001b
mov bl,00011101b
shrd al,bl,1

## Slide 18: What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and Unpacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 19: Shift and Rotate Applications
Shifting Multiple Doublewords
Binary Multiplication
Displaying Binary Bits
Isolating a Bit String

## Slide 20: Shifting Multiple Doublewords
Programs sometimes need to shift all bits within an array, as one might when moving a bitmapped graphic image from one screen location to another.
The following shifts an array of 3 doublewords 1 bit to the right (view complete source code):
.data
ArraySize = 3
array DWORD ArraySize DUP(99999999h) ; 1001 1001...
.code
mov esi,0
shr array[esi + 8],1 ; high dword
rcr array[esi + 4],1 ; middle dword, include Carry
rcr array[esi],1 ; low dword, include Carry

## Slide 21: Isolating a Bit String
The MS-DOS file date field packs the year, month, and day into 16 bits:
mov ax,dx ; make a copy of DX
shr ax,5 ; shift right 5 bits
and al,00001111b ; clear bits 4-7
mov month,al ; save in month variable
Isolate the Month field:

## Slide 22: What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and Unpacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 23: Multiplication and Division Instructions
MUL Instruction
IMUL Instruction
DIV Instruction
Signed Integer Division
CBW, CWD, CDQ Instructions
IDIV Instruction
Implementing Arithmetic Expressions

## Slide 24: MUL Instruction
In 32-bit mode, MUL (unsigned multiply) instruction multiplies an 8-, 16-, or 32-bit operand by either AL, AX, or EAX.
The instruction formats are:
    MUL r/m8
    MUL r/m16
    MUL r/m32

## Slide 25: MUL Examples
100h * 2000h, using 16-bit operands:
.data
val1 WORD 2000h
val2 WORD 100h
.code
mov ax,val1
mul val2 ; DX:AX = 00200000h, CF=1
The Carry flag indicates whether or not the upper half of the product contains significant digits.
mov eax,12345h
mov ebx,1000h
mul ebx ; EDX:EAX = 0000000012345000h, CF=0
12345h * 1000h, using 32-bit operands:

## Slide 26: IMUL Instruction
IMUL (signed integer multiply ) multiplies an 8-, 16-, or 32-bit signed operand by either AL, AX, or EAX
Preserves the sign of the product by sign-extending it into the upper half of the destination register
Example: multiply 48 * 4, using 8-bit operands:
mov al,48
mov bl,4
imul bl ; AX = 00C0h, OF=1
OF=1 because AH is not a sign extension of AL.

## Slide 27: IMUL Examples
Multiply 4,823,424 * -423:
mov eax,4823424
mov ebx,-423
imul ebx ; EDX:EAX = FFFFFFFF86635D80h, OF=0
OF=0 because EDX is a sign extension of EAX.

## Slide 28: DIV Instruction
The DIV (unsigned divide) instruction performs 8-bit, 16-bit, and 32-bit division on unsigned integers
A single operand is supplied (register or memory operand), which is assumed to be the divisor
Instruction formats:
    DIV reg/mem8
    DIV reg/mem16
    DIV reg/mem32
Default Operands:

## Slide 29: DIV Examples
Divide 8003h by 100h, using 16-bit operands:
mov dx,0 ; clear dividend, high
mov ax,8003h ; dividend, low
mov cx,100h ; divisor
div cx ; AX = 0080h, DX = 3
Same division, using 32-bit operands:
mov edx,0 ; clear dividend, high
mov eax,8003h ; dividend, low
mov ecx,100h ; divisor
div ecx ; EAX = 00000080h, DX = 3

## Slide 30: Signed Integer Division (IDIV)
Signed integers must be sign-extended before division takes place
  fill high byte/word/doubleword with a copy of the low byte/word/doubleword's sign bit
For example, the high byte contains a copy of the sign bit from the low byte:

## Slide 31: CBW, CWD, CDQ Instructions
The CBW, CWD, and CDQ instructions provide important sign-extension operations:
  CBW (convert byte to word) extends AL into AH
  CWD (convert word to doubleword) extends AX into DX
  CDQ (convert doubleword to quadword) extends EAX into EDX
Example:
    .data
    dwordVal SDWORD -101 ; FFFFFF9Bh
    .code
    mov eax,dwordVal
    cdq ; EDX:EAX = FFFFFFFFFFFFFF9Bh

## Slide 32: IDIV Instruction
IDIV (signed divide) performs signed integer division
Same syntax and operands as DIV instruction
Example: 8-bit division of –48 by 5
mov al,-48
cbw ; extend AL into AH
mov bl,5
idiv bl ; AL = -9, AH = -3

## Slide 33: IDIV Examples
Example: 32-bit division of –48 by 5
mov eax,-48
cdq ; extend EAX into EDX
mov ebx,5
idiv ebx ; EAX = -9, EDX = -3
Example: 16-bit division of –48 by 5
mov ax,-48
cwd ; extend AX into DX
mov bx,5
idiv bx ; AX = -9, DX = -3

## Slide 34: Unsigned Arithmetic Expressions
Some good reasons to learn how to implement integer expressions:
  Learn how do compilers do it
  Test your understanding of MUL, IMUL, DIV, IDIV
  Check for overflow (Carry and Overflow flags)
Example: var4 = (var1 + var2) * var3
; Assume unsigned operands
mov eax,var1
add eax,var2 ; EAX = var1 + var2
mul var3 ; EAX = EAX * var3
jc TooBig ; check for carry
mov var4,eax ; save product

## Slide 35: Signed Arithmetic Expressions (1 of 2)
Example: eax = (-var1 * var2) + var3
mov eax,var1
neg eax
imul var2
jo TooBig ; check for overflow
add eax,var3
jo TooBig ; check for overflow
Example: var4 = (var1 * 5) / (var2 – 3)
mov eax,var1 ; left side
mov ebx,5
imul ebx ; EDX:EAX = product
mov ebx,var2 ; right side
sub ebx,3
idiv ebx ; EAX = quotient
mov var4,eax

## Slide 36: Signed Arithmetic Expressions (2 of 2)
Example: var4 = (var1 * -5) / (-var2 % var3);
mov eax,var2 ; begin right side
neg eax
cdq ; sign-extend dividend
idiv var3 ; EDX = remainder
mov ebx,edx ; EBX = right side
mov eax,-5 ; begin left side
imul var1 ; EDX:EAX = left side
idiv ebx ; final division
mov var4,eax ; quotient
Sometimes it's easiest to calculate the right-hand term of an expression first.

## Slide 37: What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and UnPacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 38: Extended Addition and Subtraction
ADC Instruction
Extended Precision Addition
SBB Instruction
Extended Precision Subtraction
The instructions in this section do not apply to 64-bit mode programming.

## Slide 39: Extended Precision Addition
Adding two operands that are longer than the computer's word size (32 bits).
  Virtually no limit to the size of the operands
The arithmetic must be performed in steps
  The Carry value from each step is passed on to the next step.

## Slide 40: ADC Instruction
ADC (add with carry) instruction adds both a source operand and the contents of the Carry flag to a destination operand.
Operands are binary values
  Same syntax as ADD, SUB, etc.
Example
  Add two 32-bit integers (FFFFFFFFh + FFFFFFFFh), producing a 64-bit sum in EDX:EAX:
    mov edx,0
    mov eax,0FFFFFFFFh
    add eax,0FFFFFFFFh
    adc edx,0 ;EDX:EAX = 00000001FFFFFFFEh

## Slide 41: Extended Addition Example
Task: Add 1 to EDX:EAX
  Starting value of EDX:EAX: 00000000FFFFFFFFh
  Add the lower 32 bits first, setting the Carry flag.
  Add the upper 32 bits, and include the Carry flag.
mov edx,0 ; set upper half
mov eax,0FFFFFFFFh ; set lower half
add eax,1 ; add lower half
adc edx,0 ; add upper half
    EDX:EAX = 00000001 00000000

## Slide 42: SBB Instruction
The SBB (subtract with borrow) instruction subtracts both a source operand and the value of the Carry flag from a destination operand.
Operand syntax:
  Same as for the ADC instruction

## Slide 43: Extended Subtraction Example
Task: Subtract 1 from EDX:EAX
  Starting value of EDX:EAX: 0000000100000000h
  Subtract the lower 32 bits first, setting the Carry flag.
  Subtract the upper 32 bits, and include the Carry flag.
mov edx,1 ; set upper half
mov eax,0 ; set lower half
sub eax,1 ; subtract lower half
sbb edx,0 ; subtract upper half
EDX:EAX = 00000000 FFFFFFFF

## Slide 44: What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and UnPacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 45: ASCII and Packed Decimal Arithmetic
Binary Coded Decimal
ASCII Decimal
AAA Instruction
AAS Instruction
AAM Instruction
AAD Instruction
Packed Decimal Integers
DAA Instruction
DAS Instruction
The instructions in this section do not apply to 64-bit mode programming.

## Slide 46: Binary-Coded Decimal
Binary-coded decimal (BCD) integers use 4 binary bits to represent each decimal digit
A number using unpacked BCD representation stores a decimal digit in the lower four bits of each byte
  For example, 5,678 is stored as the following sequence of hexadecimal bytes:
05
06
07
08

## Slide 47: ASCII Decimal
A number using ASCII Decimal representation stores a single ASCII digit in each byte
  For example, 5,678 is stored as the following sequence of hexadecimal bytes:
35
36
37
38

## Slide 48: AAA Instruction
The AAA (ASCII adjust after addition) instruction adjusts the binary result of an ADD or ADC instruction. It makes the result in AL consistent with ASCII decimal representation.
  The Carry value, if any ends up in AH
Example: Add '8' and '2'
mov ah,0
mov al,'8' ; AX = 0038h
add al,'2' ; AX = 006Ah
aaa ; AX = 0100h (adjust result)
or ax,3030h ; AX = 3130h = '10'

## Slide 49: AAS Instruction
The AAS (ASCII adjust after subtraction) instruction adjusts the binary result of an SUB or SBB instruction. It makes the result in AL consistent with ASCII decimal representation.
  It places the Carry value, if any, in AH
Example: Subtract '9' from '8'
mov ah,0
mov al,'8' ; AX = 0038h
sub al,'9' ; AX = 00FFh
aas ; AX = FF09h, CF=1
or al,30h ; AL = '9'

## Slide 50: AAM Instruction
The AAM (ASCII adjust after multiplication) instruction adjusts the binary result of a MUL instruction. The multiplication must have been performed on unpacked BCD numbers.
mov bl,05h ; first operand
mov al,06h ; second operand
mul bl ; AX = 001Eh
aam ; AX = 0300h

## Slide 51: AAD Instruction
The AAD (ASCII adjust before division) instruction adjusts the unpacked BCD dividend in AX before a division operation
.data
quotient BYTE ?
remainder BYTE ?
.code
mov ax,0307h ; dividend
aad ; AX = 0025h
mov bl,5 ; divisor
div bl ; AX = 0207h
mov quotient,al
mov remainder,ah

## Slide 52: What's Next
Shift and Rotate Instructions
Shift and Rotate Applications
Multiplication and Division Instructions
Extended Addition and Subtraction
ASCII and UnPacked Decimal Arithmetic
Packed Decimal Arithmetic

## Slide 53: Packed Decimal Arithmetic
Packed decimal integers store two decimal digits per byte
  For example, 12,345,678 can be stored as the following sequence of hexadecimal bytes:
12
34
56
78
Packed decimal is also known as packed BCD.
Good for financial values – extended precision possible, without rounding errors.

## Slide 54: DAA Instruction
The DAA (decimal adjust after addition) instruction converts the binary result of an ADD or ADC operation to packed decimal format.
  The value to be adjusted must be in AL
  If the lower digit is adjusted, the Auxiliary Carry flag is set.
  If the upper digit is adjusted, the Carry flag is set.

## Slide 55: DAA Logic
If (AL(lo) > 9) or (AuxCarry = 1)
AL = AL + 6
AuxCarry = 1
Else
AuxCarry = 0
Endif
If (AL(hi) > 9) or Carry = 1
AL = AL + 60h
Carry = 1
Else
Carry = 0
Endif
If AL = AL + 6 sets the Carry flag, its value is used when evaluating AL(hi).

## Slide 56: DAA Examples
Example: calculate BCD 35 + 48
mov al,35h
add al,48h ; AL = 7Dh
daa ; AL = 83h, CF = 0
Example: calculate BCD 35 + 65
mov al,35h
add al,65h ; AL = 9Ah
daa ; AL = 00h, CF = 1
Example: calculate BCD 69 + 29
mov al,69h
add al,29h ; AL = 92h
daa ; AL = 98h, CF = 0

## Slide 57: DAS Instruction
The DAS (decimal adjust after subtraction) instruction converts the binary result of a SUB or SBB operation to packed decimal format.
The value must be in AL
Example: subtract BCD 48 from 85
mov al,48h
sub al,35h ; AL = 13h
das ; AL = 13h CF = 0

## Slide 58: DAS Logic
If (AL(lo) > 9) OR (AuxCarry = 1)
AL = AL − 6;
AuxCarry = 1;
Else
  AuxCarry = 0;
Endif
If (AL > 9FH) or (Carry = 1)
AL = AL − 60h;
Carry = 1;
Else
Carry = 0;
Endif
If AL = AL - 6 sets the Carry flag, its value is used when evaluating AL in the second IF statement.

## Slide 59: DAS Examples (1 of 2)
Example: subtract BCD 48 – 35
mov al,48h
sub al,35h ; AL = 13h
das ; AL = 13h CF = 0
Example: subtract BCD 62 – 35
mov al,62h
sub al,35h ; AL = 2Dh, CF = 0
das ; AL = 27h, CF = 0
Example: subtract BCD 32 – 29
mov al,32h
add al,29h ; AL = 09h, CF = 0
daa ; AL = 03h, CF = 0

## Slide 60: Summary
Shift and rotate instructions are some of the best tools of assembly language
  finer control than in high-level languages
  SHL, SHR, SAR, ROL, ROR, RCL, RCR
MUL and DIV – integer operations
  close relatives of SHL and SHR
  CBW, CDQ, CWD: preparation for division
32-bit Mode only:
  Extended precision arithmetic: ADC, SBB
  ASCII decimal operations (AAA, AAS, AAM, AAD)
  Packed decimal operations (DAA, DAS)